Building Cluster of 2 nodes ProxmoxV4
This method is an adaptation of https://pve.proxmox.com/wiki/Proxmox_VE_4.x_Cluster in order to avoid having a block “Waiting of quorum...” during the “pvecm add” of the second node.
The problem occurs when the nodes don't have a multicast connection (it is the case with a non configurable cheap switch).
Therefore the connection must be configurated as unicast.
## on Proxmox1:
Install of “omping” (not necessary)
aptitude install omping
config /etc/hosts as follow (replacing “proxmox1&2” by the real host name, “domain.tld” by the real domain and with their real IPs) and reboot:
127.0.0.1 localhost.localdomain localhost
192.168.2.160 proxmox1.domain.tld proxmox1 pvelocalhost

192.168.2.150 proxmox2.domain.tld proxmox2

# The following lines are desirable for IPv6 capable hosts
::1 localhost ip6-localhost ip6-loopback
ff02::1 ip6-allnodes
ff02::2 ip6-allrouters
Build the cluster
root@proxmox1:~# pvecm create cluster-GuedeL
Corosync Cluster Engine Authentication key generator.
Gathering 1024 bits for key from /dev/urandom.
Writing corosync key to /etc/corosync/authkey.
- Have a check: /etc/corosync isn't empty any more
  root@proxmox-miniitx:~# ls /etc/corosync/
  authkey corosync.conf
  and nano /etc/corosync/corosync.conf and /etc/pve/corosync.conf give the same:
  totem {
    version: 2
    secauth: on
    cluster_name: cluster-GuedeL
    config_version: 1
    ip_version: ipv4
    interface {
      ringnumber: 0
      bindnetaddr: 192.168.2.160
    }
  }

  nodelist {
    node {
      ring0_addr: proxmox-miniitx
      name: proxmox-miniitx
      nodeid: 1
      quorum_votes: 1
    }
  }

  quorum {
    provider: corosync_votequorum
  }

  logging {
    to_syslog: yes
    debug: off
  }
- Configure transmission unicast (see https://forum.proxmox.com/threads/proxmox4-cluster-2-nodes-problem-with-quorum.25445/):
  - check that /etc/pve/corosync.conf is writable (see https://www.guedel.eu/dokuwiki/doku.php?id=Welcome:Proxmox:Cluster#Delete%20the%20cluster%20config%20of%20the%20removed%20node)
    ls -l /etc/pve
  - save a copy of /etc/pve/corosync
    cp /etc/corosync/corosync.conf /etc/pve/corosync.conf.orig
  - create a modified file
    cp /etc/corosync/corosync.conf /etc/pve/corosync.conf.modif
    nano /etc/pve/corosync.conf.modif
    and add “expected_votes: 1” and “two_node: 1” into the section “quorum” and “transport: udpu” into the section “totem” in order to obtain:
    logging {
      debug: off
      to_syslog: yes
    }

    nodelist {
      node {
        name: proxmox-miniitx
        nodeid: 1
        quorum_votes: 1
        ring0_addr: proxmox-miniitx
      }

      node {
        name: proxmox-asrock
        nodeid: 2
        quorum_votes: 1
        ring0_addr: proxmox-asrock
      }

    }

    quorum {
      expected_votes: 1
      provider: corosync_votequorum
      two_node: 1
    }

    totem {
      cluster_name: cluster-GuedeL
      config_version: 2
      ip_version: ipv4
      secauth: on
      transport: udpu
      version: 2
      interface {
        bindnetaddr: 192.168.2.160
        ringnumber: 0
      }

    }
Don't forget to increment each time /etc/pve/corosync.conf is modified the value of “config_version” into the section “totem”

  - activate the modified file:
    cp /etc/pve/corosync.conf.modif /etc/pve/corosync.conf
    and reboot.
## on Proxmox2:
Install of “omping” (not necessary)
aptitude install omping
config /etc/hosts as follow (replacing “proxmox1&2” by the real host name, “domain.tld” by the real domain and with their real IPs) and reboot:
127.0.0.1 localhost.localdomain localhost
192.168.2.150 proxmox2.domain.tld proxmox2 pvelocalhost

192.168.2.160 proxmox1.domain.tld proxmox1

# The following lines are desirable for IPv6 capable hosts
::1 localhost ip6-localhost ip6-loopback
ff02::1 ip6-allnodes
ff02::2 ip6-allrouters
add this machine to the cluster (replace by the IP of Proxmox1):
pvecm add 192.168.2.160
## Troubleshooting / general infos
### Links
- proxmox cluster: https://pve.proxmox.com/wiki/Proxmox_VE_4.x_Cluster
- Multicast (for proxmoxV3): https://pve.proxmox.com/wiki/Multicast_notes#Use_unicast_instead_of_multicast_.28if_all_else_fails.29
- Cluster file system: http://pve.proxmox.com/wiki/Proxmox_Cluster_file_system_%28pmxcfs%29
- Manpage of corosync: http://manpages.ubuntu.com/manpages/maverick/man5/corosync.conf.5.html
### Configure broadcast instead of multicast
This method https://forum.proxmox.com/threads/waiting-for-quorum-in-proxmox-ve-4-0-beta-2.23551/page-2 Post #27 didn't work by me: I had further a “waiting for quorum...”.
### Remove a node from the cluster
Shutdown the node to be removed and from another node staying into the cluster:
pvecm delnode node_to:be_removed
### Delete the cluster config of the removed node
- Delete the ssh-keys and hosts from /root/.ssh.
  rm /root/.ssh/*
  works if all can be deleted.
- Delete the key of corosync:
  rm /etc/corosync/authkey
- Delete /etc/pve/corosync.conf:
  - if /etc/pve/corosync is writable, simply delete it
  - if /etc/pve/corosync is not writable (http://pve.proxmox.com/wiki/Proxmox_Cluster_file_system_%28pmxcfs%29)
    service pve-cluster stop
    pmxcfs -l
    rm /etc/pve/corosync.conf
    service pve-cluster stop
    service pve-cluster start ## some errors can occur!!
    service pvedaemon restart
    service pveproxy restart
    service pvestatd restart
    restart
    systemctl status pve-cluster.service ## should be without errors now
modifying or deleting /etc/corosync/corosync.conf seems to have no influence on /etc/pve/corosync.conf